Firmware notes rd 2
Lighthouse_position_est.c
- static void estimatePositionSweeps(const pulseProcessor_t* appState, pulseProcessorResult_t* angles, int baseStation)
  - will call estimatePositionSweepsLh2 for us
- static void estimatePositionSweepsLh2(const pulseProcessor_t* appState, pulseProcessorResult_t* angles, int baseStation) {
  - Assigns bsCalib
    - bsGeometry is a type, but I’m not sure wh
  - creates a varaible newData field (lighthouseCalibration_t type pointer), which changes the pulseProcessor_t
    - lighthouseCalibration_t type is defined within: srcutils/interface/lighthouse/lighthouse_types.h
      - This thing stores 2 lighthouseCalibrationSweep_t which is a phase, tilt, curve, gibmag, gibphase, ogeemag, ogeephase, along with a uid (uint32_t), and a valid field (boolean).
# Changing Sensor Position
src/modules/src/lighthouse/lighthouse_position_est.c
multiply all SENSOR_POS_W by -1 to flip it upside down.

# Tests Run
### No changes to firmware
Estimate position sweeps LH2 (performed at line 334 in lighthoue_position_est.c)
sweepInfo.rotorRot[0]0: -0.104769
1: -0.762651
2: -0.638268
[1]0: 0.0
1: 0.721370
2: -0.216500
[2]0: -0.423685
1: 0.879555
2: 0.0