Firmware notes rd 2

lighthouseCoreTask()
- calls → lighthouseTransmitProcessFrame(frame)
  - I think this only calls timing stuff
- calls → processFrame(&lighthouseCoreState, &angles, &frame, now_ms)
  - calls → usePulseResult(appstate, angles, basestation, sweepId, now_ms)
    - calls → pulseProcessorApplyCalibration(appState, angles, baseStation)
    - calls → convertV2AnglestoV1 angles(angles)
      - calls →
    - calls → usePulseResultsSweeps(appState, angles, baseStation)
      - calls → lighthousePositionEstimatePoseSweeps(appState, angles, baseStation)
        - calls → estimatePositionSweeps(state, angles, baseStation)
        - calls → estimateYaw(state, angles, baseStation)
  - calls → useCalibrationData(appState)

from estimatePositionSweeps()
calls → estimatePositionSweepsLh2(appState, angles, baseStation

Function processes
lighthousePositionEstimatePoseSweeps()
calls →estimatePositionSweepsLh2()

usePulseResult()
calls → usePulseResultCrossingBeams()

Notes about function processes
- lightouseCoreState = type of pulseProcessor, which holds bsCalibration, bsGeometry, bsGeoCache
  - bsGeoCache is the rotation matrices we’d like to edit
estimatePositionSweepsLh2 relies on angles from calculateAngles pulse
lighthousePositionEstimatePose

# Lighthouse_position_est.c
- static void estimatePositionSweeps(const pulseProcessor_t* appState, pulseProcessorResult_t* angles, int baseStation)
  - will call estimatePositionSweepsLh2 for us
### estimatePositionSweepsLh2
- static void estimatePositionSweepsLh2(const pulseProcessor_t* appState, pulseProcessorResult_t* angles, int baseStation) {
- Operation steps:
  1. Instantiate a sweepInfo variable (sweepAngleMeasurement_t type)
    1. Creates rotation matrices as well. It’d be a good idea to debug this, and print out what the rotation matrices look like at a given measurement.
    2. This is then passed in information from the appState, angles, and basestation passed in at function beginning.
  2. Pass sweepInfo information from appState
    1. rotorPosition origin, and rotation matrix come from basestation calibration
  3. Creates a new measurement (pulseProcessorSensorMeasurement_t instance), and passes in angles measurements.

    - bsGeometry is an object with an origin and a matrix vector
  - creates a varaible newData field (lighthouseCalibration_t type pointer), which changes the pulseProcessor_t
    - lighthouseCalibration_t type is defined within: src/utils/interface/lighthouse/lighthouse_types.h
      - This thing stores2 2 lighthouseCalibrationSweep_t which is a phase, tilt, curve, gibmag, gibphase, ogeemag, ogeephase, along with a uid (uint32_t), and a valid field (boolean).
How do I add in new parameter groups? It’d be nice to debug different stuff
# Changing Sensor Position
src/modules/src/lighthouse/lighthouse_position_est.c
multiply all SENSOR_POS_W by -1 to flip it upside down.

# Tests Run
### No changes to firmware
Estimate position sweeps LH2 (performed at line 334 in lighthoue_position_est.c)
sweepInfo.rotorRot[0]0: -0.104769
1: -0.762651
2: -0.638268
[1]0: 0.0
1: 0.721370
2: -0.216500
[2]0: -0.423685
1: 0.879555
2: 0.0

lighthouseCoreTask()
calls → lighthouseTransmitProcessFrame(frame)
I think this only calls timing stuff
calls → processFrame(&lighthouseCoreState, &angles, &frame, now_ms)
calls → usePulseResult(appstate, angles, basestation, sweepId, now_ms)
calls → pulseProcessorApplyCalibration(appState, angles, baseStation)
calls → convertV2AnglestoV1 angles(angles)
calls → usePulseResultsSweeps(appState, angles, baseStation)
calls → lighthousePositionEstimatePoseSweeps(appState, angles, baseStation)
calls → estimatePositionSweeps(state, angles, baseStation)
calls → estimateYaw(state, angles, baseStation)
calls → useCalibrationData(appState)